## Slide 1: Digital Electronics & Firmware Development for High Energy Physics Today: Introduction to CMS Trigger Rest of the week: Hands-On Firmware Work
Sridhara Dasu, University of Wisconsin

## Slide 2: The Large Hadron Collider

## Slide 3: CMS Detector

## Slide 4: Proton-Proton Collisions at the LHC
 | 2015-16 | 2012 | 2011
Beam energy | 6.5 TeV | 4.0 TeV | 3.5 TeV
Bunches/ beam | 2556 | 1380 | 1380
Protons/ bunch | 2.5x1011 | 2.2x1011 | 1.5x1011
N pp Collisions Created | ~1015 | 3.5 x 1014 | 2.5 x 1014
N Higgs Events | ~103 | ~few 102 | ~102
Fetch me my needle buried in those hay stacks –
And, do it As Soon As Possible
1 event in 10 000 000 000 000 !
Notes: 1 barn = 10-24 cm-2
Proton c.s 40mb/110mb@7TeV

## Slide 5: LHC Physics @ 13 TeV – Trigger Challenge
Electroweak Symmetry Breaking Scale
  Higgs discovery and higgs sector characterization
  Quark, lepton Yukawa couplings to higgs
New physics at TeV scale to stabilize higgs sector
  Spectroscopy of new resonances (SUSY or otherwise)
  Find dark matter candidate
Multi-TeV scale physics (loop effects)
  Indirect effects on flavor physics (mixing, FCNC, etc.)
    Bs mixing and rare B decays
  Lepton flavor violation
    Rare Z and higgs decays
Planck scale physics
  Large extra dimensions to bring it closer to experiment
  New heavy bosons
  Blackhole production
Low PT g, e, m
Low PT B, t jets
Multiple low PT objects
Missing ET
Low PT leptons
High PT leptons and photons
Multi particle and jet events
~ Dedicated triggers (CMS) or experiment (LHCB)
Low  40 GeV

## Slide 6: Trigger Task – Complex Decision in few ms

## Slide 7: LHC Physics & Event Rates
L = 1.5 x1034cm-2s-1
  40 pp events/25 ns xing
    ~ 1 GHz input rate
    “Good” events contain ~ 40 background overlap
  1 kHz W events
  10 Hz top events
  < 104 detectable Higgs decays/year
Can store ~ 1000 Hz events
Select in stages
  Level-1 Triggers
    1 GHz (pp-interactions) to 100 kHz
  High Level Triggers
    100 kHz to 1000 Hz

## Slide 8: Collisions (p-p) at LHC
Event size: ~ 1 M bytes
Event Rate: ~ 30 M Hz
All charged tracks with pt > 2 GeV
Reconstructed tracks with pt > 25 GeV
Operating conditions:
one “good” event (e.g Higgs in 4 muons )
+ ~40 minimum bias piledup events)
Event rate

## Slide 9: Processing LHC Data
QCD

## Slide 10: LHC Trigger & DAQ Challenges
Computing Services
16 Million channels
Charge
Time
Pattern
40 MHz
COLLISION RATE
100 - 50 kHz
1 MB EVENT DATA
1 Terabit/s
READOUT
50,000 data
channels
200 GB buffers
~ 400 Readout
memories
3 Gigacell buffers
500 Gigabit/s
5 TeraIPS
~ 400 CPU farms
Gigabit/s
SERVICE LAN
Petabyte ARCHIVE
Energy
Tracks
300 Hz
FILTERED
EVENT
EVENT BUILDER.
A large switching network (400+400 ports) with total throughput ~ 400Gbit/s forms the interconnection between the sources (deep buffers) and the destinations (buffers before farm CPUs).
EVENT FILTER.
A set of high performance commercial processors organized into many farms convenient for on-line and off-line applications.
SWITCH NETWORK
LEVEL-1
TRIGGER
DETECTOR CHANNELS
Challenges:
1 GHz of Input Interactions
Beam-crossing every 25 ns with ~ 23 interactions produces over 1 MB of data
Archival Storage at about 300 Hz of 1 MB events

## Slide 11: Level 1 Trigger Data

## Slide 12: L1 @ LHC: Only Calorimeter & Muon – No Tracker
Simple Algorithms
Small amounts of data
Complex Algorithms
Huge amounts of data
High Occupancy in high granularity tracking detectors
New tracker and track trigger envisioned for HL-LHC

## Slide 13: Example: Scintillator Signal
Photomultiplier serves as the amplifier
Measure if pulse height is over a threshold
from H. Spieler “Analog and Digital Electronics for Detectors”

## Slide 14: Many Steps of Processing Before Readout!
Amplifier
Filter
Shaper
Range compression
clock
Sampling
Digital filter
Zero suppression
Buffer
Format & Readout
Buffer
Feature extraction
Detector / Sensor
to Data Acquisition System
L1 Trigger Logic
L2 Trigger Logic

## Slide 15: Filtering & Shaping
Purpose is to adjust signal for the measurement desired
  Broaden a sharp pulse to reduce input bandwidth & noise
    Make it too broad and pulses from different times mix
  Analyze a wide pulse to extract the impulse time and integral ⇒
Example: Signals from scintillator every 25 ns
  Need to sum energy deposited over 150 ns
  Need to put energy in correct 25 ns time bin
  Apply digital filtering & peak finding
    Will return to this example later

## Slide 16: Sampling & Digitization
Signal can be stored in analog form or digitized at regular intervals (sampled)
  Analog readout: store charge in analog buffers (e.g. capacitors) and transmit stored charge off detector for digitization
  Digital readout with analog buffer: store charge in analog buffers, digitize buffer contents and transmit digital results off detector
  Digital readout with digital buffer: digitize the sampled signal directly, store digitally and transmit digital results off detector
  Zero suppression can be applied to not transmit data containing zeros
    Creates additional overhead to track suppressed data
Signal can be discriminated against a threshold
  Binary readout: all that is stored is whether pulse height was over threshold

## Slide 17: Range Compression
Rather than have a linear conversion from energy to bits, vary the number of bits per energy to match your detector resolution and use bits in the most economical manner.
  Have different ranges with different nos. of bits per pulse height
  Use nonlinear functions to match resolution

## Slide 18: Baseline Subtraction
Wish to measure the integral of an individual pulse on top of another signal
  Fit slope in regions away from pulses
  Subtract integral under fitted slope from pulse height

## Slide 19: EM Calorimeter Trigger/DAQ Processing
Trigger Tower
25 Xtals (TT)
TCC
(LLR)
CCS
(CERN)
SRP
(CEA
DAPNIA)
DCC
(LIP)
TCS
TTC
Trigger primitives @800 Mbits/s
OD
DAQ
@100 kHz
L1
Global TRIGGER
Calo TRIGGER
Layer-1,2, DMUX
Trigger Tower Flags (TTF)
Selective Readout Flags (SRF)
SLB (LIP)
Data path
@100KHz (Xtal Datas)
Trigger Concentrator Card
Synchronisation & Link Board
Clock & Control System
Selective Readout Processor
Data Concentrator Card
Timing, Trigger & Control
Trigger Control System
Level 1 Trigger (L1A)
From : R. Alemany LIP

## Slide 20: ECAL Trigger Primitives
Test beam results (45 MeV per xtal):

## Slide 21: Level 1 Trigger Organization

## Slide 22: CMS Calorimeter Geometry
EB, EE, HB, HE map to 18 RCT crates
Provide e/g and jet, t, ET triggers
Channel Count Full granularity: ~81000
Trigger level: ~5000

## Slide 23: Xilinx Field Programmable Gate Arrays

## Slide 24: FPGA Slice
Array of well defined logic cells, driven by LUTs
Software configured connections
Cleverly organized
Preconfigured digital logic elements

## Slide 25: Configurable Logic Block
Firmware developer uses programming languages to define “connections”
Firmware tools create the “bit file” which defines the switch matrix / LUTs

## Slide 26: Abundant Logic Resources in Virtex-7 Family

## Slide 27: Scaling: Modular Blocks of Various Resources

## Slide 28: Key element - Multi-gigabit Opto-electronics

## Slide 29: Xilinx FPGAs – Phase-1 Choice: V7 690T
Phase-1 Choice
Phase-2 Target

## Slide 30: Xilinx – Ultrascale+ for Phase-2

## Slide 31: Multi-gigabit-per-second serial links
Phase-1
10 Gbps
Phase-2
16 Gbps

## Slide 32: Channels – Channels - Channels
Geometry | h-divisions | f-divisions | Bits/E,H-tower ET, feature | Bandwidth (Gbps) | Fiber Count 4.8 – 6.4 Gbps
Barrel +/- | 17+17 | 72 | 8+1+8+6 | 2252 | 324 + 306
Endcap +/- | 11+11 | 72 | 8+1+8+6 | 1457 | 198 + 198
Total | 56 | 72 | 23 | 3609 | 1026
Calorimeter Trigger Input from ECAL and HCAL (Phase-1)
Geometry | h-divisions | f-divisions | Bits/E-crystal Bits/H-tower | Bandwidth (Gbps) | Fiber Count 16 Gbps
ECAL Crystals | 17x5 | 72x5 | 10 | 208080 | 3060
HCAL Towers | 16 | 72 | 8+6 | 645 | 144
Total | - | - | - | 208745 | 3204
Barrel Calorimeter Trigger Input from ECAL and HCAL (Phase-2)
18 cards, 1 FPGA/card, ~56 4.8-6.4-Gbps inputs per card
36 cards, 1 FPGA/card, 89 16-Gbps inputs per card

## Slide 33: Technologies of Choice  LHC Schedules
FPGA & Telecom technology advances (VME  mTCA)
  Ubiquitous >10 Gbps links
  FPGAs with O(100) rx/tx links with built in serdes
    Xilinx Kintex / Virtex-7  Ultrascale platforms
    Gigantic cores
    DSP units, BRAM and Embedded processors (ZYNQ)
  Fiber optic components
    Avago mini-pods with 12x  25 Gbps capable units
LHC long shutdown 1: 2013-2014 (Phase-1 Upgrades)
  Virtex-7 family cards
    CTP7 (Wisconsin), MP7 (Imperial), MTF7 (Florida)
  10 Gbps optics
LHC long shutdown 3: 2023-2025 (Phase-2 Upgrades)
  Ultrascale family card(s): APDs Wisconsin
  14-16 Gbps optics

## Slide 34: Phase-1 Calorimeter Trigger Electronics
Calorimeter Trigger Processor(CTP7 – left), and Master Processor (MP7 - right)
  CTP7 (Layer-1) – mTCA Single Virtex 7 FPGA, 67 optical inputs, 48 outputs, 12 RX/TX backplane
    Virtex 7 allows 10 Gb/s link speed on 3 CXP(36 TX & 36 RX) and 4 MiniPODs (31 RX & 12 TX)
    ZYNQ processor running Xilinx PetaLinux for service tasks, including virtual JTAG cable
  MP7 (Layer-2) – mTCA Single Virtex 7 FPGA, up to 72 input & output links
    Virtex 7 has 72 input and output links at 10 Gb/s
    Dual 72 or 144MB QDR RAM clocked at 500 MHz
MMC
Power Supplies
ZYNQ
FPGA
JTAG
USB
Interface
Rx
Tx
Rx
Tx
FPGA
1V0
2xQDR
(Bottom)
2V5
3V3
1V5
1V8
mSD
USB
mC
(Bottom)
MiniPODs
3 CXP modules
MiniPod modules
Notes: oRSC – optical Receiver Summary Card
CTP7 – Calorimter Trigger Processor
MP7 ?

## Slide 35: Xilinx Software – Vivado  Firmware

## Slide 36: Xilinx ZYNQ – System on a Chip  Controls

## Slide 37: 2016 CMS Trigger
CMS was built for a maximum sustainable trigger rate of 100 kHz
  To increase this requires major detector upgrades (e.g. tracker)
CMS wanted to keep its sensitivity to EWK physics, TeV scale searches, Heavy-Ion phenomena
  Solution: increase level-1 trigger granularity, processing capacity, flexibility
CMS upgraded the trigger (including the muon trigger system)
  Kept thresholds low, efficiencies high, and controlled the rates
  Commissioned in parallel to existing trigger
Took advantage of new technology
  Used modern FPGAs with high-speed links
    Fast links and increased data throughput
    Improved the algorithms
  Used modern mTCA format
    Compact (fits in spare rack space), hot swappable, redundant power supplies, high-speed backplane, control via LAN, and more…

## Slide 38: Level-1 Trigger Block Diagram (2016)

## Slide 39: Phase-1 Cal Trigger Stage-1 Upgrade in 2015
RCT 0
RCT 1
RCT 2
RCT 17
…
oRSC 0
oRSC 1
oRSC 2
…
oRSC 17
Existing RCT
18 crates
MP7 (new)
Algorithm Card(s) (1-3)
Imperial HW + Core FW/SW
USCMS Algorithm FW/SW
CTP7
Single Readout Card
In Situ RCT Test / Monitor
USCMS HW/FW/SW
Global Trigger (existing)
GT Inputs remain unchanged
DAQ – AMC 13 (new)
18 oRSCs (w/Kintex)
Layer-1
Layer-2
USCMS

## Slide 40: Phase-1 Cal Trigger Stage-2 Upgrade in 2016
MP7 Algorithm Cards (9+1)
Imperial HW + FW/SW
USCMS Algorithm FW/SW
mTCA Global Trigger
DAQ – AMC13
DAQ – AMC 13
Layer-1
Layer-2
CTP–0
CTP–1
CTP–2
CTP–17
…
18 CTP7s
USCMS
Full flexibility for traditional or time-multiplexed architecture
TMT – in use now.
Highest precision location of objects with dynamic clustering

## Slide 41: VME Hardware (2015) for Calorimeter Trigger

## Slide 42: CMS Calorimeter Trigger 2016
Installed and commissioned in 2015, fully operational in 2016
  Connections to CTP7 from Layer-1 patch panels completed in 2015
  Connections from Layer-1 to Layer-2 via compact patch panel
    3 “pizza box” sized patch panels instead of full 56U rack with LC connectors
  Layer 2 to demux to new mGT connected
Layer-1 CTP7
Layer-2 MP7
MOLEX
FlexPlane
Layer-1 to Layer-2 Patch Panel

## Slide 43: CMS Calorimeter Trigger 2016
Installed and commissioned in 2015, fully operational in 2016
  ECAL Back End (BE) has been converted to optical (from Cu) with Mezzanines
    2 x 4.8 Gbps links each, one for 2015 operation, one to Layer-1 Patch Panels
  HF and HCAL BE has been replaced with optical back end (mHTR)
    6.4 Gbps links, up to 6 per mHTR
  All optical connections to Layer-1 complete
    1152 fibers to 18 patch panels for conversion to MPO fiber ribbons
ECAL
New HCAL and HF BE
BE to Layer1
Patch Panels

## Slide 44: Calorimeter Trigger Algorithms
Overall
  Use full calorimeter tower granularity
    Previously 14h x18f now 56h x 72f
    Better energy & position resolution
  Cluster dynamically
  Mitigate pileup
e/g
  Cluster shape and electromagnetic energy fraction discriminates e/g from jets
  Energy weighted position to potentially use for invariant mass triggers
Tau
  Clustering and position similar to e/g, optimized for tau
  Merge neighboring clusters to recover multi-prong tau decays
Jet
  Sliding window, search for seed (central tower) energy above threshold
  Remove duplicates, sum 9 by 9 trigger towers for ~R=0.4 as used offline
2010 to 2015
2016 onwards

## Slide 45: e/g Algorithm
Dynamic Clustering
  Improved energy containment Showing electrons, photon conversions Minimize effect of pile-up Improved energy resolution
Cluster Shape Veto
  Discriminate using cluster shape and electromagnetic energy fraction between e/γ and jets
Calibration
  e/γ cluster energy calibrated as a function of ET, η and cluster shape
Energy Weighted Position
  Potential use in correlating objects e.g. invariant mass
Cluster Building
Cluster Shapes
Jet like
e/g like

## Slide 46: Tau Algorthm
Clustering, shape, and position
  Very similar to e/γ — optimised for τ
Merging
  Merge neighbouring clusters (~15% of clusters) Recover multi-prong τ decays
Calibration
  τ cluster energy calibrated as function of ET, η, merging and EM fraction
Isolation
  Very similar to e/γ — optimised for tau including merging as input – two working points

## Slide 47: Jet Algorithm
Input Granularity
  Access to higher granularity inputs than Run I
Sliding window jet algorithm
  Search for seed energy above threshold Apply veto mask to remove duplicates Sum 9x9 trigger towers to approximate R=0.4 used offline
Pile-Up Subtraction
  Consider four areas around jet window Subtract sum of energy in lowest three from jet energy
Calibration
  Correct jet energies as a function of jet ET and η
Pile-up Subtraction Areas
Seed Tower
Veto Mask

## Slide 48: e/g Performance
Efficiency for single e/g with ET > L1 threshold vs offline ET
  Tag and probe method with Zee dataset
  As LHC conditions change, isolation adapted
  Isolated e/g reduces rate with modest reduction in efficiency
    Combined with higher-threshold non-iso triggers
Isolated e/g
Better Position Resolution
Non-Isolated e/g

## Slide 49: Tau Performance
Efficiency for a single tau for ET> L1 threshold vs offline tau pT
  Tag and probe for Zmt
  Adapt isolation as LHC conditions change
  Isolated reduces rate with modest impact on efficiency
    Can be combined with higher-threshold relaxed tau trigger
Isolated tau
Relaxed tau

## Slide 50: Jet Performance
Level-1 jets are matched to offline jets (DR < 0.25)
  Single muon data sample (unbiased)
  Sharp turn on for different L1 Jet ET (upper left)
  No pile up dependence (upper right)
  Good resolution (right)