## Slide 1: Triggering CMS Physics in the HL-LHC environment
12 August 2020

## Slide 2: LHC Overview
with every bunch crossing
~25 Minimum Bias events
with ~2000 particles produced
Notes: 10 Trillion

## Slide 3: HL-LHC Overview
with every bunch crossing
~200 Minimum Bias events
with ~10000 particles produced
7.5x
2x
Notes: 10 Trillion

## Slide 4: HLLHC Parameters
Operating at 2x now
Expect Operating at 7.5x ultimately

## Slide 5: HLLHC Physics & Event Rates
At L = 7.5 x 1034 cm-2 s-1
  200 events per beam crossing (BX)
    ~ 7.5 GHz pp collision rate
    “Interesting” events contain ~ 200 pileup events
  EWK rate: 7.5 kHz W & Z
  Top rate: 75 Hz
  Higgs: 1 Hz, H4l: 10–4 Hz
Select in stages
  Level-1 Triggers
    7.5 GHz (32 MHz BX ) to 750 kHz
  High Level Triggers
    750 kHz to ~10 kHz
Event store: ~10 kHz events
Scale shifts up by 7.5x

## Slide 6: (HL) LHC Physics – Trigger Challenge
Electroweak Symmetry Breaking Scale
  Higgs (125 GeV) studies and higgs sector characterization
  Quark, lepton Yukawa couplings to higgs
New physics at TeV scale to stabilize higgs sector
  Spectroscopy of new EWK produced resonances (SUSY or otherwise)
  Find dark matter candidate
Multi-TeV scale physics (loop effects)
  Indirect effects on flavor physics (mixing, FCNC, etc.)
    Bs mixing and rare B decays
  Lepton flavor violation
    Rare Z and higgs decays
Planck scale physics
  Large extra dimensions to bring it closer to experiment
  New heavy bosons
  Blackhole production
Low PT g, e, m
Low PT B, t jets
Multiple low PT objects
Missing ET
Low PT leptons
High PT leptons and photons
Multi particle and jet events
~ Dedicated triggers (CMS) or experiment (LHCB)
Low  30 GeV

## Slide 7: Collisions (p-p) at HLLHC
Selecting high PT clusters and tracks
Can not afford to go any higher in thresholds!

## Slide 8: Requirements (my slide from Feb 2004)
Track trigger !
Crystal readout !!

## Slide 9: Planning ahead (my slide from July 2005)

## Slide 10: CMS HLLHC Level-1 Trigger 2020
New for HLLHC

## Slide 11: Triggers  Physics

## Slide 12: Getting the crystal data out (New for HLLHC)
There are 61200 crystals to be processed – packing 25 crystals per link out of BCP you still have 2448 links at 16 Gbps to contend in the calorimeter trigger path!

## Slide 13: Getting the tracks out (New for HLLHC)
Divide and conquer
In space and time
Outer tracker double layers allow track stub readout
Tracklets formed in TFP consistent with >2GeV PT propagated in-out, matched to form track candidates
Tracklets are then fit to make a track

## Slide 14: Bits and Pieces from Everywhere

## Slide 15: Many Multi-gigabit Optical Links

## Slide 16: Challenges: Pile-up
Redoing frontend electronics for faster response

## Slide 17: Challenges: Time of Flight
c = 30 cm/ns → in 25 ns, s = 7.5 m
Building in TDCs to exploit timing information to mitigate pileup

## Slide 18: Processing HLLHC Data
QCD
Commercial Processors (600ms – 1s)
Custom Processors (ms)

## Slide 19: Xilinx Field Programmable Gate Arrays

## Slide 20: Xilinx – Ultrascale+ for Phase-2
In Use Now
For HLLHC

## Slide 21: Key element - Multi-gigabit Opto-electronics

## Slide 22: The APx Consortium
Pooling of efforts in ATCA Processor hardware, firmware and software development
Multiple ATCA processors and mezzanine board types
Modular design philosophy, emphasis on platform solutions with flexibility and expandability
Reusable circuit, firmware and software elements

## Slide 23: APd1 Rev B
Eight APd1 RevB boards built
  Boards setup to make a significant communication protocol test.
APd1: 100 28 G optical links each
  76 on main board
  24 on Rear Transition Module
40.08 MHz Clock + BC0
  Via “ersatz TCDS” (3.2 G link)
  Sourced from AMC13 + CTTP7
  Delivered via front panel SFP
Linux Hostname: ”SparrowX”
TIFR built IPMC & ESM mezzanines
ELM ZYNQ mezzanine

## Slide 25: APx – Firmware/Software
A new paradigm for firmware development
  Core firmware written in VHDL by engineers
  Gigabit link support
  Data exchange between SLRs within chip
  Test buffers
  Clock and control
Physics
  Algorithmic firmware in high-level languages like C++ written by physicists
ELM:
Control endpoint,
providing complete
board overhead
functionality
Processing FPGA:
I/O
data processor
DAQ

## Slide 26: APx Firmware Shell

## Slide 27: APx-FS Resource Utilization
APd1 VU9P FPGA floorplan
100x 25G GTY links w/ support infra
Central AXI infra with MGT-based Chip2chip core
VU9P build

## Slide 28: Multi-Card HLS Demonstrators
Gen-0 (in operation at UW and CERN)
  CTP7-based (3 cards, 96 total active links @ 10.0G available)
  HLS interface grafted onto Phase 1 8b10b link infrastructure
  64-bit link interfaces
Gen-1 (in operation at UW)
  APd1 single card setup
  Iridis-style 64b66b transport
  Early APx shell functionality
    Asynchronous processing clock
Gen-2 (in operation at UW)
  Multicard test setup (Several 100 25 Gbps links)
  Iridis-style signaling and APx shell environment
  Common emulated TCDS timebase in ATCA/MicroTCA crates using CTP7

## Slide 29: Gen-1 Demonstrator Firmware
Algorithm block interface standardized on AXI-stream for input and output data
  Build time configurable number of input and output links
  Designed such to allow direct instantiation of HLS IP block (option A)
  Also an option to include HDL wrapper inside the algo block (option B)
H
D
L
H
D
L
HLS
HLS
Option A
Option B
Algo Block
Algo Block

## Slide 30: Example Algorithm - from U of Hyderabad

## Slide 31: Use of C++ & High Level Synthesis

## Slide 32: Timing & Latency

## Slide 33: Particle Flow Reconstruction on FPGAs

## Slide 34: Particle Flow Implementation in Barrel

## Slide 35: Particle Flow Resource Utilization on VU9P

## Slide 36: Concluding Thoughts
A team of engineers and physicists are taming the LHC data deluge with intelligent use of communications technologies to enable fundamental physics discoveries.
Advances in telecommunications technologies are continually adapted to track increasing data streams.
Students and postdocs are getting good training, especially in writing algorithmic firmware, for potential careers in both academia and industry.
Sincere Thanks to: Engineering Team: Tom Gorski, Ales Svetek, Jesra Tikalsky, Robert Fobes (UW), Luis Morena (Princeton), Mandakini Patil, Kushsal Bhalerao (TIFR) Physics Collaborators: Wesley Smith, Sascha Savin, Isobel Ojalvo, Bhawna Gomber, Varun Sharma, Kajari Mazumdar, Jeff Berryhill, Rick Cavanaugh, Dylan Rankin