## Slide 1: Physics 535 Particles & Detectors
Passage of Particles Through Matter

## Slide 2: True or False?
A high energy (~1GeV) photon is traversing vacuum – could it convert to an electron-photon pair?:
True or False ?
A high-energy (~1 GeV) electron is traversing vacuum in a straight line – could it lose energy by emitting photons?:
True or False ?
A high-energy (~1 GeV) electron is traversing vacuum in a circular synchrotron – could it lose energy by emitting photons?: True or False ?

## Slide 3: True or False?
A high energy (~1GeV) photon impinges on a chunk of metal – could it convert to an electron-photon pair?:
True or False ?
A high-energy (~1 GeV) photon impinges on a chunk of metal – it converts to an electron and positron each with energy equal to ~0.5 GeV?: True or False ?
A 100-MeV electron impinges on a crystal – could it lose energy by emitting photons?:
True or False ?

## Slide 4: True or False?
Both 100 MeV and above electrons and photons produce a cascade of electrons and photons?:
True or False ?
The photons stop converting to electron-positron pairs when they have E < 2me: True or False ?
Muon is a heavier lepton compared to an electron. Its electromagnetic interactions with matter occur at the same rate as that of an electron?:
True or False ?

## Slide 5: Interaction of Particles in CMS

## Slide 6: Scattering Cross Section for Heavy Charged Particle w/ Electrons
For particles with charge, ze, and mass, m>>me, speed, v=bc, energy, E, is lost in a collision due to ionization, atomic or collective excitation

## Slide 7: Moments of Cross Section

## Slide 8: Energy Loss of Muons

## Slide 9: Energy loss for Muons, Pions, Protons

## Slide 10: Material Dependence of dE/dx

## Slide 11: Range of Relativistic Particles
For 1 GeV muons range in Fe is ~5000 g-cm-2 / 8 g-cm-3
~6 meters!

## Slide 12: Energy Loss Distribution

## Slide 13: Energy Loss Distributions of p±

## Slide 14: Restricted Energy Loss Most Probable Energy Loss
In thin detector elements, probability of large losses is low
  So, restricted (Tcut < Tmax) energy loss is useful
  Most probable energy loss (Dp/x) is much smaller than dE/dx

## Slide 15: Energetic Knock-On Electrons d-rays
Although rare, high energy, i.e. much greater than mean energy loss, T>>I, electrons can be knocked out of the material, with distribution:
δ rays of even modest energy are rare.
For a β ≈ 1 particle, on average only one collision with Te>10 keV will occur along a path length of 90 cm of Ar gas.

## Slide 16: Multiple Coulomb Scattering
Charged particle scattering from nuclear EM field

## Slide 17: Particle Detectors

## Slide 18: Interaction of Particles in Detectors (CMS)
Which of the following particle types are able to ionize the detector material?
  Photons
  Neutral Hadrons
  Charged Hadrons
  Electrons & Positrons
  Muons
The momentum of charged pions can be measured using?
  Tracker and the magnet
  Calorimeters and the magnet
  Tracker and the calorimeters
  Tracker, the magnet and the gas chambers in the iron return yoke
  Gas chambers and the magnet
Which of these particles is not measurable in CMS?
  Photons
  Hadrons
  Electrons & Positrons
  Muons
  Neutrinos

## Slide 19: Charged Particle Trackers
Magnetic Field
  Solenoidal field from 1 to 4 Tesla field
  Lengths from 0.6 to 6 m
Tracking Detectors measure “hits” recorded along helical path
  Ionization energy in gases measured in wire chambers
  Ionization energy in silicon using strip (or pixel) diodes
Resolution of track momentum depends on B and L

## Slide 20: Electromagnetic Showers
From Sven Menke

## Slide 21: Radiation Length
High-energy electrons predominantly lose energy in matter by bremsstrahlung, and high-energy photons by e+e− pair production
The characteristic amount of matter traversed for these related interactions is called the radiation length X0, usually measured in g cm−2
  The mean distance over which a high-energy electron loses all but 1/e of its energy by bremsstrahlung
  7/9 of the mean free path for pair production by a high-energy photon

## Slide 22: Electron Energy Loss Fractions
Ec

## Slide 23: Photon Scattering Cross Sections

## Slide 24: Electromagnetic Shower
Eg >1.5 MeV

## Slide 25: Longitudinal Shower Development

## Slide 26: Moliere Radius
Transverse development of EM showers is fit using
  Moliere Radius:
  On average only ~10% of energy is outside RM
  On average only ~1% of energy is outside 3.5RM
  Distribution:

## Slide 27: EM Calorimeters
Better than 1% energy resolution possible for 100 GeV electrons & photons

## Slide 28: Hadronic Interaction Length
The length scale appropriate for hadronic cascades is the nuclear interaction length, given very roughly by
  Length to first interaction
    Typically p0 created (decays to photons) with EM shower (Interaction probability in one lI is 63%)
    Hadronic debris continues to develop showers
    Spreads more longitudinally & transversely
    Hadronic shower maximum:

## Slide 29: Hadronic Calorimeter Thickness
Containment of hadronic showers takes large calorimeters
Energy resolution depends on the thickness ratio of active/passive, light-yield, photo-detector …
Energy resolutions vary between 50%/√E and 100 % /√E

## Slide 30: Muon Systems
Muon systems are usually large magnetized steel structures interspersed with gas chambers
  Drift tubes
  Resistive plate chambers
  Cathode strip chambers
Sparse point measurements sufficient
  Occupancy is usually low
Matching of muon system tracks to the inner tracks provides good measurement
  Multiple scattering needs to be taken account

## Slide 31: CMS Muon/Tracker Resolution

## Slide 32: 8-GeV Spectrometer @ SLAC Deep Inelastic Scattering (eP)

## Slide 33: The Detectors in the 8-GeV Spectrometer
June – September 1985
Calibration of toroids (for beam energy)
Spectrometer survey, Cherenkov & Calorimeter rebuilt
New electronics, data acquisition, software … online display of cross section result!
(MWPC from E139)

## Slide 34: Electronics Le Croy ADC/TDCs & Cable Delay Lines

## Slide 35: The e-p Discrimination

## Slide 36: SLD Detector on SLC (e+e-)

## Slide 37: CCD Pixel Vertex Detector + Cerenkov Ring Imaging Detector

## Slide 38: ZEUS Detector @ DESY

## Slide 39: ZEUS U-Scintillator Calorimeter

## Slide 40: BaBar Detector at SLAC

## Slide 41: BaBar - DIRC

## Slide 42: The LZ TPC in Sanford (SD) for Dark Matter Searches